## Slide 1: Federated Learning in V2X Communications for Side-link Enhancement
Junjie Wu
2021.12.31

## Slide 2
We consider the scenario of federated learning in V2X communications. The vehicles that demand the same AI model shall participate in federated learning through wireless communications in order to train an accurate global model. We focus on the side-link enhancement and further consider the use case of power control where deep reinforcement learning (DRL) is applied to minimize average power consumption of data transmission while satisfying delay constraint.
Figure. 1 Side-link communication in V2X.
Federated Learning in V2X Communications for Side-link Enhancement
Scenario，Problem & Proposal
  Scenario:
Figure. 2 System diagram of federated learning in V2X communications.

## Slide 3
Scenario, Problem& Topics
Transmitter
(SCMA)
Far User
Near User
Far codeword
decoder
Near codeword
decoder
Far codeword
interference
cancellation
For vehicles lacking consensus of environment (similarity of dataset), the model quality may be reduced due to aggregation process with the risk of adding irrelevant data samples, especially for reinforcement learning which requires a feedback from the dynamic environment. What’s more, the performance of federated learning suffers from the “straggler”. Therefore, how to group FL users and allocate resources becomes a major problem, especially for federated training of DRL based side-link power control.
Scenario，Problem & Proposal
  Problem:
  Proposal:
Figure. 3 DRL based side-link power control in V2X.
Federated Learning in V2X Communications for Side-link Enhancement
FL
Grouping 1
Grouping 2
Figure. 4 Schematic diagram of FL grouping.
The vehicles upload their sidelink information in addition to assistance information such as location, uplink channel state, etc. to gNB. The gNB decides the training group based on the sidelink information and allocate resources based on assistance information.
FL

## Slide 4
Specification from the 3GPP
  1. SA Plenary 94#E Work Item: 5G System Support for AI/ML-based Services (SP-211613, approved):
  Objective 3 (WT#1.3): Study whether and how 5GS provides assistance to AF and the UE for the AF and UE to manage the FL operation and model distribution/redistribution (i.e. FL members selection, group performance monitoring, adequate network resources allocation and guarantee.) to facilitate collaborative Application AI/ML based Federated Learning operation between the application clients running on the UEs and the Application Servers.).
  2. TS 22.186 Enhancement of 3GPP support for V2X Scenario
  [R.5.1-002] The 3GPP system shall be able to optimize the communication between UEs supporting V2X application belonging to the same group and in proximity.
  [R.5.1-009] The 3GPP system shall support efficient coordination of radio resources used for transport of messages to maximize the utilization of the available spectrum and to ensure the required reliability.
  ---- Our patent considers FL for the enhancement of sidelink in V2X. The grouping is based on sidelink information which introduces new signalings in uplink. To mitigate the “straggler effect”, resources allocation is considered with assistance information (new signalings as well).

## Slide 5
Federated Learning
Model aggregation: global model
Local model uploading
Local model
Local model uploading
Local model uploading
Local model
Local model
Sidelink communication
Scenario and Problem
Scenario:
Federated learning in V2X Side-link

## Slide 6
Scenario and Problem
Problem:
Model
environment 1
Probability distribution of channel state
Federated Training
Model
environment 2
Probability distribution of channel state
More Similar environment: Good
Less Similar environment: Bad
Model
environment 1
Probability distribution of channel state
Federated Training
Model
environment 3
Probability distribution of channel state
2. Straggler effect: everyone waits for the slowest vehicles to update the model.
1. Different environment results in heterogeneity of dataset for devices, leading to the degradation of FL performance. (This is even worse when deep reinforcement learning is applied, e.g. Use cases in Page)

## Slide 7
Solution
Grouping & UE selection
Gather sidelink information, S
i –th Vehicle UE
Measure the similarity between DRL models based on ,…, ].
gNB
Upload the samples of S: ,…, ]
(2) Group DRL models with high similarity.
Solve the problem of data heterogeneity: choose similar environment
1. S is the sidelink information, which could be the channel busy ratio (already existed), RSRP, RSRQ, RSSI, SNR, CSI, NLOS/LOS), etc. We specifically add the probability distribution of channel state as the new content. Details are given in the following slides
New signaling content to add in MeasResultsSL (TS 38.331)
2. There are many measurements for the similarity, such as KL divergence (given in P25), etc.
Note:

## Slide 8
Solution
MeasResultsSL information element
MeasResultsSL-r16 ::= SEQUENCE {
measResultsListSL-r16 CHOICE {
measResultNR-SL-r16 MeasResultNR-SL-r16,
...
},
...
}
MeasResultNR-SL-r16 ::= SEQUENCE {
measResultListCBR-NR-r16 SEQUENCE (SIZE (1.. maxNrofSL-PoolToMeasureNR-r16)) OF MeasResultCBR-NR-r16,
measResultListPDCS-NR SEQUENCE (XXXXX)
measResultListOther-NR SEQUENCE (XXXXX)
...
}
Add new signaling “measResultListPDCS-NR” in MeasResultsSL to transmit the probability distribution of channel state ,…,] in sidelink i, where is the probability that sidelink is in channel state
The detail of why transmitting the probability distribution of channel state is shown in the following sildes Page 9 and Page 10
Add new signaling “measResultListOther-NR” in MeasResultsSL to transmit other sidelink information such as RSRP, RSRQ, RSSI, SNR, CSI, NLOS/LOS, channel statistics (e.g., mean, variance), etc

## Slide 9
Use case: side-link power control
Scenario: Power Control for Delay-Power Tradeoff
Physical
Layer
Data link Layer
server
Network Layer
…
…
Adaptive Power Control
Channel
State (CSI)
Channel state
Channel state
Channel state
…
…
s.t.
s.t.
MDP （Markov Decision Problem)
--- average delay
--- average power
--- threshold of power
--- threshold of delay

## Slide 10
Data Queue
Tx
Rx
Wireless Channel
Deep Reinforcement Learning（DRL)
Channel State (CSI)
Power & Rate adaptive
Data Arrival
Solution: Deep Reinforcement Learning based Power Control
Use case: side-link power control
Environment of DRL
Notes: Since the optimal power control of sidelink can be formulated as an MDP, we can implement Deep Reinforcement Learning (DRL) to exactly solve MDP, i.e., the optimal power control problem. To achieve better joint training effect, we shall choose similar DRL models as a group to train together. Fortunately, in the sidelink power control problem, the stochastic environment of DRL is wireless channel. Therefore, the probability distribution of channel state can uniquely identify the characteristics of DRL model. We can describe the similarity of DRL models using the similarity of the probability distributions of the channel states. As a result, the probability distribution of channel state is essential for choosing the similar DRL models as the grouping process in FL.

## Slide 11
Gather assistance information, A
Upload A
According to the assistance information uploaded by UE, gNB allocates resources for UEs’ local modal uploading e.g., find the heavy-weighted straggler (slow but significant) and allocate more resource.
Solution
FL Resource Allocation
Mitigate the straggler effect
i –th Vehicle UE
gNB
Note:
1. A is the assistance information. In addition to the local information, it contains more information: computational capability (e.g. CPU occupancy), training data size, etc.
2. Heavy-weighted straggler: UE that has more weights in the model aggregation process but with slow updating. E.g. an UE with
1). heavy data(i.e., large training data set) --- > contribute more
2). high priority --- > need to participate the training
3). worse CPUs --- > computation latency
4). located far --- > transmission delay.
3. gNB has to allocate more resources to the “straggler” vehicle to reduce its transmission latency

## Slide 12
Gather assistance information, A
Training based on the basic model
Upload A
According to the assistance information uploaded by UE, gNB allocates resources for UEs’ local modal uploading e.g., find the heavy-weighted straggler (slow but significant) and allocate more resource.
Solution
FL Process
Gather sidelink information, S
i –th Vehicle UE
Measure the similarity between DRL models based on ,…, ].
gNB
Upload the samples of S: ,…, ]
(2) Group DRL models with high similarity.
Global model
Resource allocation information
gNB aggregates the local models to get the global model.
Upload the local model

## Slide 13
To solve the problem of data heterogeneity, a proper selection of UE is required in FL. The side-link information of the probability distribution of channel state is uploaded to the gNB as the basis for FL UE-vehicle selection. The transmission is done via the uplink. Although the uplink transmission of sidelink information is supported in R16. Therefore new signaling is introduced.
Summary
The straggler effect is a problem exclusively in FL. To mitigate it, resource allocation is applied to reduce the transmission latency of the straggler. This process involves uploading some assistance information as new signalings (e.g. CPU occupany, training data size, etc)

## Slide 14
Solution: Joint Training of DRL Model through Federated Learning
(1) Training in Single DRL Model
DRL Model
environment
,…,]
Probability distribution of channel state
Reward
Updating of Queue Length
Power Consumption
Action
Transmission Power
(2) Federated Training in Multi DRL Models
DRL Model 1
environment 1
,…,]
Probability distribution of channel state
Federated Training
DRL Model 2
environment 1
,…,]
Probability distribution of channel state
DRL Model 1
environment 1
,…,]
Probability distribution of channel state
Federated Training
DRL Model 2
environment 2
,…,]
Probability distribution of channel state
Good
Bad
Different environment results in heterogeneity of dataset for devices, leading to the degradation of FL performance.
Use case: side-link power control

## Slide 15
Federated Learning
Model aggregation: global model
Local model uploading
Power Control for sidelink
Communication
DRL
Local model:
Local model uploading
Local model uploading
DRL
Local model:
DRL
Local model:
Sidelink power control
Power Control for sidelink
Communication
Power Control for sidelink
Communication
Use case: side-link power control

## Slide 16
Distributed Federated Learning for Ultra-Reliable Low-Latency Vehicular Communications Sumudu Samarakoon , Member, IEEE,
Mehdi Bennis , Senior Member, IEEE, Walid Saad , Fellow, IEEE, and Mérouane Debbah, Fellow, IEEE
FL in Vehicular Networks: Queuing Management in Side-link
Appendix: Literature Research
V2V Communications in different environments
Queuing Management based on FL

## Slide 17
Liu B, Wang L, Liu M. Lifelong federated reinforcement learning: a learning architecture for navigation in cloud robotic systems[J]. IEEE Robotics and Automation Letters, 2019, 4(4): 4555-4562.
Framework: Federated Reinforcement Learning
Federated Reinforcement Learning (FRL)
Appendix: Literature Research

## Slide 18
Federated Learning for 6G: Applications, Challenges, and Opportunities https://arxiv.org/abs/2101.01338
Federated Reinforcement Learning (FRL)
Application: Multi-Cell Power Control Problem
Appendix: Literature Research

## Slide 19
Appendix: Motivation
[1] Distributed Federated Learning for Ultra-Reliable Low-Latency Vehicular Communications Sumudu Samarakoon , Member, IEEE,
Mehdi Bennis , Senior Member, IEEE, Walid Saad , Fellow, IEEE, and Mérouane Debbah, Fellow, IEEE
[2] Liu B, Wang L, Liu M. Lifelong federated reinforcement learning: a learning architecture for navigation in cloud robotic systems[J]. IEEE Robotics and Automation Letters, 2019, 4(4): 4555-4562.
[3] Federated Learning for 6G: Applications, Challenges, and Opportunities https://arxiv.org/abs/2101.01338
Enhance Queuing Management of Side-link through FL
Train multi DRL models together through FL
Implement DRL in power control
In [1], FL was implemented in queuing management of side-link, in which queue-length-bound violation probability was finally minimized
In [2], the concept and framework of FRL were proposed, based on which FL can be used to jointly train multiple DRL models
In [3], the FRL were implemented in Multi-Cell power control problem to maximize the total throughput
We implement DRL in adaptive power control to enhance queuing management of side-link in achieving the optimal delay-power tradeoff. The DRL models can be trained together through FL to speed up the training process and share training samples.

## Slide 20
Elbir, Ahmet M., Burak Soner, and Sinem Coleri. "Federated Learning in Vehicular Networks." arXiv preprint arXiv:2006.01412 (2020).
FL in Vehicular Networks: Pros & Cons
Background
Benefits:
Compared with traditional ML training in Vehicular Network, users in FL only need to upload the Local AI model (Gradient) instead of the dataset. This reduces communication overheads and protects privacy and security
Challenges:
1. Efficient model training --- the model quality may be reduced due to aggregation process with the risk of adding irrelevant data samples
2. Scheduling and resource management --- how to mitigate the straggler effect, i.e., in each iteration the aggregation has to wait for the slowest UEs (probably with unfavorable links or limited computational capabilities)

## Slide 21
Federated learning (FL) in V2X communications receives more and more attention from academia and industry, due to the large demands for AI model in V2X such as unmanned driving, route optimization, collision prevention and so on. The vehicles that demand the same AI model shall participate in federated learning through wireless communications in order to train an accurate global model.
Figure. 1 The demands for AI model in V2X.
Local model
Sample data
AI Training
Location
Size of data
& Location
uploading
Power
& resource
allocation
Global
model
downloading
Parameters
uploading
Figure. 2 Behaviors of single vehicle in FL.
Background
Applying FL in Vehicular Networks

## Slide 22
Elbir, Ahmet M., Burak Soner, and Sinem Coleri. "Federated Learning in Vehicular Networks." arXiv preprint arXiv:2006.01412 (2020).
FL in Vehicular Networks: Motivations
Motivations for FL in Vehicular Networks
Background
Compare with traditional ML training in Vehicular Network, users in FL only need to upload the Local AI model (Gradient) instead of the dataset.

## Slide 23
FL-Related
Research Challenges
Data Diversity
Labeling
Efficient Model Training
Communications-Related Research Challenges
Transmission Overhead
Delay
Security and Privacy
Scheduling and Resource Management
FL in Vehicular Networks：Challenges
Background
Elbir, Ahmet M., Burak Soner, and Sinem Coleri. "Federated Learning in Vehicular Networks." arXiv preprint arXiv:2006.01412 (2020).

## Slide 24
Scheduling and Resource Management
(1) Device heterogeneity and spatial distribution
(2) Frequent and sporadic handovers
Efficient Model Training
Transfer learning is used to solve the problem of heterogeneous
machine learning model in FL
(2) Transfer learning accuracy strongly relies on the similarity between
the target model and the pre-trained model.
Background
Elbir, Ahmet M., Burak Soner, and Sinem Coleri. "Federated Learning in Vehicular Networks." arXiv preprint arXiv:2006.01412 (2020).
FL in Vehicular Networks：Challenges

## Slide 25
Introduction to KL divergence
What is KL divergence
The KL divergence is an information-theoretic measure introduced by Kullback and Leibler in 1951, and quantifies the discrepancy between two information sources or random variables. The KL divergence plays significant roles in information theory and various disciplines such as statistics, machine learning, physics, neuroscience, computer science, linguistics, etc.
Mathematical form of KL divergence
For two probability distributions,
,…,]
,…,]
KL divergence between two probability distributions can be represented as

## Slide 26
Scenario and Solution
Example for grouping based on probability distribution of CSI in side-link
(2) FL Grouping based on Similarity Measurement
(1) KL divergence based similarity measurement
Probability distributions of CSI:
,…,]
,…,]
Similarity measurement based on KL divergence:
For probability distributions of CSI: if then
DRL Model 1
environment 1
Probability distribution of channel state
Federated Training
DRL Model 2
environment 2
Probability distribution of channel state
More Similar environment: Good
Less Similar environment: Bad
DRL Model 1
environment 1
Probability distribution of channel state
Federated Training
DRL Model 2
environment 3
Probability distribution of channel state