## Slide 1: D2D-aided model splitting
AI/ML operation splitting between AI/ML endpoints
Scenario:
Network partition is fixed
Solution:
Offload part of Model A from UE1 to UE2
Standard impact:
S1-220183 Study on AI/ML Model Transfer_Phase2
Objective: Distributed AI training/inference based on Device to Device connection, e.g. traffic KPIs, different QoS and functional requirements on slidelink transmission.
Scenario 1:
1). Good sidelink (UE 1 <--> UE 2)
2). Good up/down-link (UE 1 <--> gNB)
3). Good up/down-link (UE 2 <--> gNB)
4). Limited computation at UE#1
5). Sufficient computation at UE#2
Service flow:
UE#1  UE#2  gNB  UE#1
Scenario 2:
1). Good sidelink (UE 1 <--> UE 2)
2). Good up/down-link (UE 1 <--> gNB)
3). Bad up/down-link (UE 2 <--> gNB)
4). Limited computation at UE#1
5). Sufficient computation at UE#2
Service flow:
UE#1  UE#2  UE#1  gNB  UE#1
Scenario 3:
1). Good sidelink (UE 1 <--> UE 2)
2). Bad up/down-link (UE 1 <--> gNB)
3). Good up/down-link (UE 2 <--> gNB)
4). Limited computation at UE#1
5). Sufficient computation at UE#2
Service flow:
UE#1  UE#2  gNB  UE#2  UE#1
Problem:
Guarantee the service when UE with limited computational capabilities
Scenario 4:
1). Good sidelink (UE 1 <--> UE 2)
2). Bad up/down-link (UE 1 <--> gNB)
3). Good up/down-link (UE 2 <--> gNB)
4). Sufficient computation at UE#1
5). Sufficient or limited computation at UE#2
Service flow:
UE#1  UE#2  gNB  UE#2  UE#1